EX9042D/9043D/9045D

# Introduction

The EX9000/ EX9000-M remote Input/ Output as Digital I/O,

Analog I/O, Relay and Counter modules.  We offer many different communication modules for data send/ receive as RS485, Modbus, Ethernet, Wireless, Fiber Optical.

Customers can select specific modes according to         Application purposes.  Data send/ receive can get from

Industry PC via safe RS485 bus or Ethernet port for

Monitoring and Controlling.

# Specification

# Text boxes

## open collector  OUTput

Output Channels            13/ EX9042D

16/ EX9043D

16/ EX9045D

Output Type                   Open Collector(NPN)/ EX9042D

Open Collector(NPN)/ EX9043D

Open drain Output / EX9045D

Isolation Voltage            3750 Vrms/ EX9042D

Non Isolation/ EX9043D

Isolation/ EX9045D

Load Volatge                  Max +30V

Max Load current	100mA / EX9042D/ EX9043D

3A/ EX9045D(per channel)

Dual Watch Dog             Yes

Digital Output                 Save Value: Yes

Power On Value: Yes                     Ouput Command Value: Yes

## Power requirement

Power input                    +10 to +30 VDC

- Power Consumption       0.8W

Order Infomation:

Optional                          Modbus

Accessories                    Din Rail/ Wall Mount

CD(Utility/ Demo/ DLL/  Library/ Manual

Wire Connection/ Block Diagram)